## Slide 1: Active-Learning Framework for On-Road Vehicle Recognition and Tracking
SUBMITTED BY :-
Puneet Saluja (2015KUCP1019)
Tanmay Sonkusle (2015KUCP1023)
DATE :- 08-09-2017

## Slide 2
Source : https://in.pinterest.com/pin/312929874079845947

## Slide 3
Source : GOVERNMENT OF INDIA MINISTRY OF ROAD TRANSPORT & HIGHWAYS TRANSPORT RESEARCH WING
Worldwide automotive accidents injure between 20 and 50 million people each year, and at least 1.2 million people die as a result of them.
(source : WHO)

## Slide 4: ABSTRACT
Active learning approach to build a vehicle recognition and tracking system.
Robust vehicle detection using Adaboost and Haar like features.
Tracking of multiple vehicles using Particle Filter.
This framework yields an accurate, reliable and efficient safety system.

## Slide 5: UNDERSTANDING YOUR SURROUNDING

## Slide 6: VISUAL SCANNING USING VIDEO CAMERA
Captures image quickly.
Less computation work.
Short range of view.
Lack of precise information of object.
Source : https://amcrest.com/video-camera-pt.html

## Slide 7: VISUAL SCANNING USING LASER
Calculates accurate distance of the object.
Calculate geometric information of the object in its field of view.
Too much computation costs.
Source : waymo.com

## Slide 8: FUSION OF LASER SCANNER AND VIDEO CAMERA
Less computation cost.
The system fuses laser scanner measurements with images of a video sensor.
Source : References[3]

## Slide 9: VEHICLE DETECTION
Source : https://www.youtube.com/watch?v=mjBKPmINEcQ

## Slide 10: HAAR LIKE FEATURES
Edge Features
Line Features
Four-rectangle features
It is a machine learning based approach where a cascade function is trained from a lot of positive and negative images.
Initially, the algorithm needs a lot of positive images (images of cars) and negative images (images without cars) to train the classifier.

## Slide 11
HAAR LIKE FEATURES ON VEHICLE
Source : https://images.cardekho.com/images/accord/Honda_Accord.png

## Slide 12: HOW IT WORKS..?
Each feature is a single value obtained by subtracting sum of pixels under white rectangle from sum of pixels under black rectangle.
Every feature is applied on all the training images.
For each feature, it finds the best threshold which will classify the cars to positive and negative.

## Slide 13: INTEGRAL IMAGE
1 | 2
3 | 4
1 | 3
4 | 10
It simplifies calculation of sum of pixels, how large may be the number of pixels, to an operation involving just four pixels.
Sum of pixels = (A+D) – (B+C)

## Slide 14: ADABOOST
Adaboost is a machine learning algorithm that helps in finding best features among all the features.
Adaboost constructs strong classifiers as a linear combination of weak classifier.
H – strong classifier
- weight of classifier
h(t) – weak classifier

## Slide 15: CASCADING
Stage 0
Stage 1
Stage n
Pass
Pass
Car
Fail
Fail
Fail
……
Feature
Feature must pass all stages in the cascade to be concluded as a vehicle.

## Slide 16: VEHICLE TRACKING
Source : waymo.com

## Slide 17: PARTICLE FILTER
Mainly used to detect/track the objects.
Used by applying different colors to different objects to remove the unnecessary particles surrounded by an object.
Source : References [1]

## Slide 18: LIKELIHOOD FUNCTION
This function is used to reduce the number of particles surrounded on the object.
Particles that lies on the object have some RGB value.
Particles that lies outside of the object have some other RGB value.
Particles which are having more weight will generate new particles near them and remaining are move on to the object.

## Slide 19: FLOWCHART
Background Image Update
Background Image Initialization
Background Subtraction
Moving Object Detection
Selected Object Tracking
Video Sequence
Selected particular object
Did not select a particular object

## Slide 20: ACTIVE-LEARNING BASED VEHICLE RECOGNITION AND TRACKING

## Slide 21: ACTIVE LEARNING
It includes discovering, processing and applying information.
Engage in learning process rather than passively absorbing information.
Using active learning yields a signiﬁcant drop in false positives per frame and false-detection rates, while maintaining a high vehicle-recognition rate

## Slide 22: INITIALIZATION
The initial passively trained Adaboost cascaded classifier was trained using 7500 positive training images and 20500 negative training images.
Positive Training Data
Negative Training Data
Source : Base Paper

## Slide 23: QUAIL
QUAIL evaluates the passively trained vehicle-recognition system on real-world data and provides an interface for a human to label and archive the ground truth.
Detection is automatically marked green
Missed detection is marked red by the user
False positives are marked blue by the user.
True detection is left green.
Source : Base Paper

## Slide 24: QUERY AND RETRAINING
Source : Base Paper

## Slide 25: EXPERIMENTAL EVALUATION
TRUE POSITIVE RATE : -
TPR =
2) FALSE DETECTION RATE
FDR =

## Slide 26: PERFORMANCE METRICES
Recognition/Tracking System | TPR | FDR
Passively Trained Vehicle Detection | 89.5% | 51.5%
ALVeRT | 95.0% | 6.4%
EXPERIMENTAL DATA SET 1: JANUARY 28, 2009, 4 P.M., San Diego (Base Paper)

## Slide 27: CONCLUSION
Selective sampling was performed using QUAIL.
Using active learning, a full vehicle-recognition and tracking system has been implemented.
In future research efforts can be made to include pedestrian-protection systems, automatic parking and to develop autonomous vehicle.

## Slide 28: REFERENCES
BASE PAPER :- Sayanan Sivaraman , “A General Active-Learning Framework for On-Road Vehicle Recognition and Tracking”, VOL. 11, NO. 2,JUNE 2010.
M.Gopi Krishna, A. Srinivasulu, “Face Detection System On AdaBoost Algorithm Using Haar Classifiers”, Vol. 2, Issue. 5, Sep.-Oct. 2012
S. Wender and K. Dietmayer, “3D vehicle detection using a laser scanner and a video camera,” IET Intell. Transp. Syst., vol. 2, no. 2, pp. 105–112, Jun. 2008.
P. Viola and M. Jones, “Rapid object detection using a boosted cascade of simple features,” in Proc. IEEE Conf. Comput. Vis. Pattern Recog., Dec. 2001, vol. 1, pp. 511–518.
Ted Talk – “Chris Urmson: How a driverless car sees the road” link – https://www.youtube.com/watch?v=tiwVMrTLUWg

## Slide 29: THANK YOU